## Slide 1
Design and Simulation of analog/RF ICs with Open-Source CAD Tools and PDKs:
All-Region Single-Piece MOSFET Theory
Pr. Carlos Galup-Montoro Department of electrical engineering Universidade Federal de Santa Catarina, Brasil

## Slide 2: Outline
Introduction: ACM timeline
ACM2 model
Long-channel: ID and gm/ID models

## Slide 3
1993 -based model (SBMICRO, Campinas, Br)
1995 Long-channel charge-based model (SSE, Nov.)
1998 Most referenced ACM paper (JSSC, Oct.)
2000 ACM model in SMASH simulator ( CICC, Orlando)
2018 Short course on ACM for ST organized by Prof. Sylvain Bourdel in Grenoble
2021 4-parameter single-piece model (NorCAS, Oslo)
2023 ACM2 in VERILOG-AMS ( NEWCAS, Edinburgh)
ACM timeline

## Slide 4: Outline
Introduction: ACM timeline
ACM2 model
Long-channel: ID and gm/ID models

## Slide 5
The capacitive model of the MOSFET
+ + + + + + + + +
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
VG
p-substrate
surface potential
+
_
+
_
Cox oxide capacitance per unit area
Cb depletion capacitance per unit area
QI carrier charge density
VT0 threshold voltage
Notes: 5

## Slide 6
ACM2 current law
From 3 approximations: normalized current vs. normalized charge densities at source and drain
normalization (specific) current
ratio of diffusion-related velocity to saturation velocity
Short-channel parameter :
thermal charge
SI : qS(D) >> 1 WI : qS(D) << 1
Notes: 6

## Slide 7
Physics-based saturation
z
y
x
W
t
ID
QDsat is the saturation inversion charge per unit area, or, using normalized variables:
vlim
vlim
vlim
vlim
vlim
Saturation current due to saturation velocity of the carriers
“Carrier velocity approaches vsat, but never reaches vsat” Y.Taur TED March 2019

## Slide 8: Physics-based saturation: design model
+
or equivalently

## Slide 9: The “Regional” Weak (WI) and Strong Inversion (SI) Approximations
The Unified Charge Control Model (UCCM)
WI SI
-
Error <10% for
Error <10% for

## Slide 10: UCCM including the effect of velocity saturation

## Slide 11: Output curves including DIBL and
Transistor | [] |  |  | n |  | 
NMOS |  | 528 | 5.52 | 1.37 | 0.025 | 0.056
Transistor |  |  |  | n |  | 
NMOS |  | 528 | 5.52 | 1.37 | 0.025 | 0.056
WI
MI
SI

## Slide 12
Total channel charge and capacitances
We can define a virtual charge that differs from the real charge by a constant term along the channel
Thus
Consequently, the virtual charge varies along the channel as the real charge in a long-channel transistor in strong inversion
=

## Slide 13
Intrinsic capacitances including velocity saturation and DIBL

## Slide 14
Sah’s formula for the thermal noise 1
For a short-channel transistor in saturation
Design-oriented formula
Thermal noise
where Qch is the channel inversion charge
1C. T, Sah et al, IEEE TED, Apr. 1966
In ACM2

## Slide 15: Outline
Introduction: ACM timeline
ACM2 model
Long-channel: ID and gm/ID models

## Slide 16: Long-channel charge-based model
=0 → =0
Obs:

## Slide 17
in saturation
Small-signal transconductances
+
Symmetry
Amazingly simple
(see Appendix)
Notes: 17

## Slide 18
(A) can also be written as
: forward (reverse) inversion coefficients
Unified Current Control Model (UICM)-I
: forward and reverse currents
(A)
(B)

## Slide 19
Normalized UICM
Unified Current Control Model (UICM)-II

## Slide 20
For VDS/t<<1 we have if  ir
In saturation if >> ir
gm/ID

## Slide 21: REFERENCES
A. I. A. Cunha, M. C. Schneider and C. Galup-Montoro,"Derivation of the Unified Charge Control Model and Parameter Extraction Procedure", Solid-State Electronics, March 1999.
O. C. Gouveia Filho, A. I. A. Cunha, M. C. Schneider and C. Galup-Montoro, "Advanced compact model for short-channel MOS transistors", IEEE Custom Integrated Circuits Conference, Orlando, FL, USA, May 2000.
C. Galup-Montoro and M. C. Schneider, MOSFET Modeling for Circuit Analysis and Design, World Scientific, 2007.
C. M. Adornes, D. G. Alves Neto, M. C. Schneider and C. Galup-Montoro, " Bridging the Gap between Design and Simulation of Low-Voltage CMOS Circuits ," Journal of Low Power Electronics and Applications, June 2022.
D. G. Alves Neto et al, ‘‘Design-oriented single-piece 5-DC parameter MOSFET model,’’ IEEE Access, 2024.

## Slide 22
Appendix: the exact model of the long-channel MOSFET1
1 H. C. Pao and C. T. Sah, ‘Effects of diffusion current on characteristics of metal-oxide (insulator)-semiconductor transistors” Solid-State Electronics, Oct 1966.
=
Consequently, the exact expressions for gms and gmd are
=

## Slide 23
Design and Simulation of analog/RF ICs with Open-Source CAD Tools and PDKs: Implementing the ACM2 model
Manuel J. Barragán
Directeur de Recherche CNRS, TIMA
Manuel.Barragan@univ-grenoble-Alpes.fr

## Slide 24: Outline
The ACM2 model (a quick recap)
Numerical solving of the UCCM equations
acm 433 algorithm and Lambert function
Analytical approximation of Lambert functions
Towards a closed-form I-V MOSFET model

## Slide 25: The ACM2 model (a quick recap)
The 5-parameter ACM2 model
Only 5 parameters: n, IS0, VT0, s and
where
with
Alves Neto ACCESS 2024

## Slide 26: The ACM2 model (a quick recap)
The 5-parameter ACM2 model
Only 5 parameters: n, IS0, VT0, s and
where
with
Alves Neto ACCESS 2024

## Slide 27: The ACM2 model (a quick recap)
Computing ID in practice:
Given the model parameters and polarization voltages
n, IS0, VT0, s and
VG, VD, VS, VB
Step 1: Compute VP:
Step 2: Compute qS:
Step 3: Compute qDsat:
Step 4: Compute qD:
Step 5: Compute ID:

## Slide 28: The ACM2 model (a quick recap)
Computing ID in practice:
Given the model parameters and polarization voltages
n, IS0, VT0, s and
VG, VD, VS, VB
Step 1: Compute VP:
Step 2: Compute qS:
Step 3: Compute qDsat:
Step 4: Compute qD:
Step 5: Compute ID:
Transcendental equations

## Slide 29: Acm 443 algorithm and Lambert W Functions
How to solve
efficiently?
Algorithm 443: Solution of the transcendental equation wew=x
Fritsch et al. Communications of the ACM, 1973

## Slide 30: Acm 443 algorithm and Lambert W Functions
How to solve
efficiently?
Algorithm 443
Fritsch et al. Communications of the ACM, 1973

## Slide 31: Acm 443 algorithm and Lambert W Functions
Can we consider the problem analytically?
The Lambert W function z = w ew for w any complex number was studied by Johann Lambert in 1758, then properly defined by L. Euler in 1783

## Slide 32: Acm 443 algorithm and Lambert W Functions
Can we consider the problem analytically?
The Lambert W function z = w ew for w any complex number was studied by Johann Lambert in 1758, then properly defined by L. Euler in 1783
For real numbers x and W(x), equation x= W(x) e W(x) has solutions W0 and W-1:
x
W(x)
x=–1/e
qS, qD and qDsat, and ID can be expressed as a function of VG, VD, Vs using W0

## Slide 33: Acm 443 algorithm and Lambert W Functions
…but can we approximate W0 in terms of elementary functions?
Expressing ID using Lamber W function
W0 is available in main programming languages: Matlab (lambertw), Octave (lambertw), Python (lambertw in scipy lib), R (lambertW0), …

## Slide 34: Acm 443 algorithm and Lambert W Functions
Approximating the Lambert W function
For real numbers x and W(x), x= W(x) e W(x)
x
W(x)
R. Iacono et al. Advances in Computational Mathematics, 2017
Approximation of W0(x)for x>0
For n=1,2,3,…
where

## Slide 35: Acm 443 algorithm and Lambert W Functions
Approximating the Lambert W function
For real numbers x and W(x), x= W(x) e W(x)
R. Iacono et al. Advances in Computational Mathematics, 2017
Approximation of W0(x)for x>0
For n=1,2,3,…
where

## Slide 36: Acm 443 algorithm and Lambert W Functions
Approximating the Lambert W function
For real numbers x and W(x), x= W(x) e W(x)
R. Iacono et al. Advances in Computational Mathematics, 2017
Approximation of W0(x)for x>0
where
Max. rel. error <4%

## Slide 37: Acm 443 algorithm and Lambert W Functions
Approximating the Lambert W function
Approximating qS
Approximating qD is similar from:

## Slide 38: Towards an analytical I-V MOSFET model
Replacing qS(VG, VS, VD,) and qD(VG, VS, VD) in ID will give a closed-form I-V model… but the expression is complex
Proposal: modified empirical model targeting closed-form I-V
J. Poupon et al., IEEE Access 2024
where

## Slide 39: Towards an analytical I-V MOSFET model
Replacing qS(VG, VS, VD,) and qD(VG, VS, VD) in ID will give a closed-form I-V model… but the expression is complex
Proposal: modified empirical model targeting closed-form I-V
J. Poupon et al., IEEE Access 2024
where

## Slide 40: Take aways
The ACM2 model contains transcendental equations
Numerical solving and/or approximations are needed
acm 433 algorithm and Lambert W function are two useful mathematical tools in this context
Happy coding!!

## Slide 41
Thank you!

## Slide 42
Design and Simulation of analog/RF ICs with Open-Source CAD Tools and PDKs:
Parameter Extraction and Circuit Simulation
Deni Germano Alves Neto PhD Student Universidade Federal de Santa Catarina, Brasil
Université Grenoble Alpes, France

## Slide 43: About me
Universidade Federal de Santa Catarina – UFSC - Brasil
Undergrad and Masters in IC design - 2022
    Dissertation: Ultra-Low-Voltage Standard Cell Library
      ACM for low voltage circuits
Contact with open-source IC design : Analog/Digital IC design
  Chipathon-SSCS 2021/2023
  UNIC-CASS 2023/2024
Joint PhD in 2023 : UFSC & UGA
  MOSFET Modeling – ACM2
  RFIC design

## Slide 44: Outline
Compact models
ACM2 model
  Parameter Extraction
  DC characteristics
  Circuit examples

## Slide 45
Why the need for a design-oriented MOSFET model ?
Medium of information exchange between foundry and designer.
Provides detailed information about device operation & characteristics.
Simple enough to be incorporated in circuit simulators.
Accurate enough to predict behavior of circuits.
Oversimplified models
Over complex Models
Poor accuracy, only in one region
2/3 DC parameters
High accuracy in all regions ?
tens of DC parameters

## Slide 46
Why the need for a design-oriented MOSFET model ?
Medium of information exchange between foundry and designer.
Provides detailed information about device operation & characteristics.
Simple enough to be incorporated in circuit simulators.
Accurate enough to predict behavior of circuits.
Bridges the gap between design and simulation!
Oversimplified models
Over complex Models
Good enough accuracy in all regions
5 DC parameters
Poor accuracy, only in one region
2/3 DC parameters
Design-oriented model: ACM2
IC designers bridge
High accuracy in all regions ?
tens of DC parameters

## Slide 47
BSIM4 issues in sky130
PSP103 issues in IHP open PDK
Subthreshold region
Modeling problem in weak inversion : Effect of DIBL on the output conductance not included

## Slide 48
Open-source PDK
Open-source EDA tools
Few open-source IP & libraries
Available compact MOSFET models
We propose: ACM2 : A Simple 5-DC-parameter MOSFET model
Open-Source IC design

## Slide 49: Outline
Compact models
ACM2 model
  Parameter Extraction
  DC characteristics
  Circuit examples

## Slide 50: ACM2: A simple 5-DC-parameter MOSFET model Complete continuous all-region charge-based MOSFET model
Specific current
(W,L)
Threshold voltage
(W,L)
Slope factor
(W,L)
DIBL factor
(W,L)
Vsat effect
(W,L)
Used to calculate
Bridge between WI and SI regions
Used to calculate
Bridge between Triode and Saturation regions

## Slide 51
where
DC equations
No saturation effect  no ,no
No DIBL effect  no
Let’s simplify and use only the 3-parameter model (no sat no DIBL)

## Slide 52: Oversimplified model vs ACM model @ Saturation
Quadratic model:
ACM Model:

## Slide 53: Output characteristics including DIBL and
Transistor | [] |  |  | n |  | 
NMOS |  | 528 | 5.52 | 1.37 | 0.025 | 0.056
Transistor |  |  |  | n |  | 
NMOS |  | 528 | 5.52 | 1.37 | 0.025 | 0.056
DIBL model:
WI
MI
SI

## Slide 54: Outline
Compact models
ACM2 model
  Parameter Extraction
  DC characteristics
  Circuit examples

## Slide 55: 3PM-ACM model in a nutshell
where
If we choose
DC eqs
Small–signal eqs
For VDS/t<<1 (triode)
In saturation

## Slide 56
, and extraction - method
For qS = 1, and gm/ID is at ½ of its maximum value
Notes: VER O ALGORITMO DE EXTRAÇÃO DESSE SLIDE

## Slide 57
extraction –
1 - C.M. Adornes et al, Journal of Low Power Electronics, 2022.
(Please see slide 136)

## Slide 58
extraction
calculated from UCCM (, , ).
Measure .
Notes: Passos do algoritmo de extração

## Slide 59
2
Verilog-A code Available!
“Scan me”
&

## Slide 60: Automatic parameter extraction tool @ XSCHEM
Available for IHP130, GF180 and SKY130

## Slide 61: Outline
Compact models
ACM2 model
  Parameter Extraction
  DC characteristics
  Circuit examples

## Slide 62: ACM2: A simple 5-DC-parameter MOSFET model
Specific current
Threshold voltage
Slope factor
DIBL factor
Vsat effect
Specific current
Slope factor
)
DIBL factor
)

## Slide 63
ACM2¹ vs meas – 130 nm SiGe IHP²
Characteristics of a LVT NMOS bulk transistor with W /L = 10μm/ 120 nm.
¹ ACM2 : implemented in verilog-A, compiled by OPENVAF, simulated in Ngspice
2 Institut for High-Performance Microelectronics (IHP) open-source PDK
mV
V

## Slide 64
ACM2¹ vs meas – 130 nm SiGe IHP² –
185mV
85 mV
V
 | PSP103 | BSIM4 | EKV2.6 | ACM2
time(s) | 3.48 | 6.7 | 0.22 | 0.15
Characteristics of a LVT NMOS bulk transistor with W /L = 10μm/ 120 nm.
¹ ACM2 : implemented in verilog-A, compiled by OPENVAF, simulated in Ngspice
2 Institut for High-Performance Microelectronics (IHP) open-source PDK
OPENVAF compilation time

## Slide 65: Outline
Compact models
ACM2 model
  Parameter Extraction
  DC characteristics
  Circuit examples

## Slide 66
CMOS Inverter in 130 nm bulk
Short-circuit current
VTC
ACM
PSP103

## Slide 67
CMOS Inverter in 28 nm FD-SOI
ACM
UTSOI2
Short-circuit current
VTC

## Slide 68
CMOS Inverter in 130 nm bulk
Output Voltage and pull-down current

## Slide 69
11-Stages Ring Oscillator 180 nm bulk
Output Voltage

## Slide 70
Self-biased current source in 180 nm bulk

## Slide 71
Common-source Amplifier in 180 nm bulk

## Slide 72
Summary – The ACM2 model
A truly compact MOSFET model with single-piece functions
Implemented in Verilog-A for simulation
  Interchangeable between simulators (SPICE or SPECTRE)
Verified in all three open-source PDKs (Sky130, GF180, IHP-SG13G2)
Helpful to designers (only 5-DC-parameters)
Simplified parameter extraction procedure
    extracted from simulations or chip measurements

## Slide 73: References
Deni Germano Alves Neto et al., "Design-Oriented Single-Piece 5-DC-Parameter MOSFET Model,” in IEEE Access, 2024.
C.M. Adornes, D.G. Alves Neto, M.C Schneider, C. Galup-Montoro,“Bridging the Gap between Design and Simulation of Low-Voltage CMOS Circuits,” Journal of Low Power Electronics, 2022.
ACM2 Github: https://github.com/ACMmodel/MOSFET_model
IHP Github : https://github.com/IHP-GmbH/IHP-Open-PDK
Available in Github:
  DC model
  Small-signal model
  Dynamic model
  Thermal &
  Flicker noise models (1/f)

## Slide 74: Appendix: Qucs-S - Quite universal circuit simulator with SPICE
VERILOG-A (Model Equations)
OPENVAF
Qucsator
XYCE
SG13G2 PDK
Simulation setup:

## Slide 75: Appendix: Qucs-S - Quite universal circuit simulator with SPICE
Ngspice simulations:
  DC
  AC
  TRAN
  S-parameters
  Noise
  Fourier
Diagram results
Tabular results
Device path for the MOS model and parameters (IHP pdk)
Circuit
Schematic
Simulations
Control
Input eqs.

## Slide 76
Design and Simulation of analog/RF ICs with Open-Source CAD Tools and PDKs:
RF Circuit Design
Pr. Sylvain Bourdel TIMA Laboratory Grenoble INP, France

## Slide 77: Agenda
Overview of Design Methods for RFIC
LNA Design Considerations
Resistive Feedback LNA
What we need in ACM-2
Inversion Level Based Method for R-Feedback LNA with ACM-2

## Slide 78: Agenda
Overview of Design Methods for RFIC
LNA Design Considerations
Resistive Feedback LNA
What we need in ACM-2
Inversion Level Based Method for R-Feedback LNA with ACM-2

## Slide 79: Overview of Design Methods for RFIC General Principle
1st Step: Architecture Choice
2nd Step: Circuit Analysis
Circuit Param.
(RL, gm, RF…)
Circuit Perf.
(GV, F, IIP3…)

## Slide 80
3rd Step: Circuit Sizing
Requirements
(GV, F, IIP3…)
Set of equation
Circuit Param.
(RL, gm, RF…)
Analytical analysis based on model
MOSFET Physical Param.
(W, L, ID)
Overview of Design Methods for RFIC General Principle

## Slide 81
3rd Step: Circuit Sizing
Requirements
(GV, F, IIP3…)
Set of equation
Circuit Param.
(RL, gm, RF…)
Analytical analysis based on model
MOSFET Physical Param.
(W, L, ID)
Overview of Design Methods for RFIC General Principle
Region based model
sat.
lin.
PROS: simple
CONS: Inaccurate with short channel MOS

## Slide 82
3rd Step: Circuit Sizing
Requirements
(GV, F, IIP3…)
Set of equation
Circuit Param.
(RL, gm, RF…)
Analytical analysis based on model
MOSFET Physical Param.
(W, L, ID)
Overview of Design Methods for RFIC General Principle
Electrical simulation based on model
BSIM3 / UTSOI compact model
PROS:
  Accurate
  Direct relationship between requirements and physical parameters
CONS:
  Increases the gap between physics and design
  Long optimization

## Slide 83: Overview of Design Methods for RFIC New Trends
Issue in the sizing step
  How to maintain simplicity and accuracy with the scaling and especially Short Channel Effects (SCE) at the sizing step.
A possible solution
  gm/Id design approaches
    LUT based
    ACM or EKV based
?
?

## Slide 84: Overview of Design Methods for RFIC gm/Id approach based on LUT
[Silveira, Flandre, Jespers – JSSC 1996]
General Principle
For a given structure

## Slide 85: Overview of Design Methods for RFIC gm/Id approach based on LUT
1
General Principle
For a given structure
Methods are based on
  Extraction of MOS parameters (LUT)
    ID/(W/L) vs gm/ID
    gm/ID vs Vgs0

## Slide 86
Overview of Design Methods for RFIC gm/Id approach based on LUT
1
2
General Principle
For a given structure
Methods are based on
  Extraction of MOS parameters (LUT)
    ID/(W/L) vs gm/ID
    gm/ID vs Vgs0
  Set of equations

## Slide 87
Overview of Design Methods for RFIC gm/Id approach based on LUT
General Principle
For a given structure
Methods are based on
  Extraction of MOS parameters (LUT)
    ID/(W/L) vs gm/ID
    gm/ID vs Vgs0
  Set of equations
Methods helps the designers in sizing the structure
Quite used in low frequency domain
1
2
3

## Slide 88
LIMITATIONS ?
Time Consuming
Lakes of precision (parametric set
of characteristics)
Long optimization sequence
Need for a model based approach
Overview of Design Methods for RFIC gm/Id approach based on LUT

## Slide 89
All Region 3PM model
EKV – [Enz, Krummenacher, Vittoz]
ACM – [Schneider, Galup]
With a 3PM model we have :
  PROS: The sizing is straightforward
  CONS: Inaccurate with SCE
      Non-linearities can’t be captured
      gds effect can’t be captured
Overview of Design Methods for RFIC gm/Id approach based All Region Models (ACM/EKV)
Can we design RFICs ?
Notes: ISQ

## Slide 90
Design Regions
ft grows with if
if
if
Overview of Design Methods for RFIC gm/Id in RFIC design
Year 2000 (RF-180nm)

## Slide 91
Design Regions
ft grows with if but gm/ID reduces with if
if
if
Overview of Design Methods for RFIC gm/Id in RFIC design
Year 2000 (RF-180nm)
Year 2016 (RF-22nm) up to now

## Slide 92
gmft/ID : A First Approach
For RF design
A FOM that maximize the gain bandwidth product
Gives the if that produces the best GBW product
Not optimal :
  the gain or the bandwidth might be oversized.
  Do not depends on the topology
Overview of Design Methods for RFIC gm/Id in RFIC design

## Slide 93
Function Based FoM
For a given Function
Define a FoM for the function
Find the if that maximizes the FoM
LNA
LO
R. Fioreli ; J. Núñez ; F. Silveira; “All-Rnversion region gm/ID methodology for RF circuits in FinFET technologies” 2018 NEWCAS
Overview of Design Methods for RFIC gm/Id in RFIC design

## Slide 94
Circuit Sizing Based on LUT
For a given Circuit
Similar to the one introduced by Silveira, Flandre, Jespers in 1996
Capacitance and noise effects can be captured in LUT for bandwidth and noise analysis
Well known and well referenced
But …
    Still complicated
    The gap between physics and design remains
    No analytical relationships to size « by hand »
Overview of Design Methods for RFIC gm/Id in RFIC design
Circuit Sizing Based on ACM
Equations can be derived for a given circuit
Quasi analytical approach
R-F LNA designed with 3PM-ACM [Bourdel - ICECS 2019]
Gds and gm3 (NL) are taken into account
  R-F LNA designed with 7PM-ACM [Bouchoucha – ISCAS 2023]
CG LNA designed with 5PM-ACM2[Alves Neto – ACCESS 2024]
All Ressources accessible for free
https://github.com/ACMmodel/MOSFET_model
Circuit Based Method
Notes: OPEN ACCES

## Slide 95: Agenda
Overview of Design Methods for RFIC
LNA Design Considerations
Resistive Feedback LNA
What we need in ACM-2
Inversion Level Based Method for R-Feedback LNA with ACM-2

## Slide 96
NF also express the quantity of noise added by the stage regarding the noise delivered by the source (Rg) on f. (Eq. 2)
Rg
Zi
Vso+Vno
NF is the signal to noise ratio (SNR) degradation (Eq. 1)
LNA Design considerations Noise Factor

## Slide 97
This formula is valid only for real impedances and in case of power matching: (Zs=Ze=Rg)
Rg
Gv: loaded voltage gain
In RFIC, impedances are complex and never equal. This formula cannot be used as is.
However, the following statements remain valid in RFIC.
The gain of the first stages reduces the NF of the following ones.
=> The receiver chain must start by amplifiers
=> The NF of the first stage must be as low as possible
Note that lossy stages (Gv<1) increase the NF, especially when they are in front
of the receiver chain (antenna filter, image rejection filter, antenna switch ).
LNA
RF Basis
LNA Design considerations Friss Formula

## Slide 98
System point of vue
LNA is the first device due to Friss formula
Antenna is mainly 50 W.
In CMOS
Generally, the input impedance is capacitive Re (Y11) is very low
For example : CS amplifier
LNA Design considerations Input patching
LNA
Antenna
Zlna=Zg*
CG
R-Feedback
Inductive Degeneration

## Slide 99
LNA Design considerations Non-Linearities
Vs
w1
w2
2w1-w2
2w2-w1
w2
w1
Vint
Vint
w1 and w2 are 2 harmonics of the wanted signal
20logVeIP3
Never reached in measurement !
Ve
The IIP3 (VeIP3) is the input signal level for which the output IM3 is equaling the fundamental harmonic (Vs) extrapolated from small signal (AC).
The IIP3 (VeIP3) is related to the maximum power you can apply to your system
Non-linear LNA
IM3

## Slide 100: Agenda
Overview of Design Methods for RFIC
LNA Design Considerations
Resistive Feedback LNA
What we need in ACM-2
Inversion Level Based Method for R-Feedback LNA with ACM-2

## Slide 101
Resistive Feedback LNA Topology
R-Feedback general considerations
Simple & Compact (No-inductors) & Wideband
RF allows to synthesize a real part in Zin
LG and CGS’ will help in cancelling the imaginary part
while controlling Qin
= 50 W
Input impedance
Reduces for
Note :

## Slide 102
Resistive Feedback LNA Topology
Voltage Gain
RS
(the source resistance seen
at the 50 W input)
Noise Figure
IIP3
BW
Notes: We are comparing of requirements and circuits parameters (variables).
GT
IIP3
Noise figure and Band width

## Slide 103: Agenda
Overview of Design Methods for RFIC
LNA Design Considerations
Resistive Feedback LNA
What we need in ACM-2
Inversion Level Based Method for R-Feedback LNA with ACM-2

## Slide 104
What we need in ACM-2 Small signal parameters
Small signal (AC) parameters
GT, NF, IIP3 vs (gm, gm3, gDS)
Valid in all region ( qs and qd shall be explored )
  We consider only saturation
  It reduces the exploration to only qs.

## Slide 105
What we need in ACM-2 Small signal parameters
Large signal (DC) parameters
To compute the final voltages
Sometimes we’ll use if in the code

## Slide 106: Agenda
Overview of Design Methods for RFIC
LNA Design Considerations
Resistive Feedback LNA
What we need in ACM-2
Inversion Level Based Method for R-Feedback LNA with ACM-2

## Slide 107
Inversion Level Based Method for R-Feedback LNA with ACM-2
General Approach :
Requirements
GT, NF, IIP3, IDC Possible Tradeoff
fo, CL, BW No Tradeoff
Design Variables (parameters)
W, qs are first order design variables (qs = inversion level sets the energy efficiency and the voltages)
RL, RF are second order design variables
Approach :
Explore the different tradeoff (the design space) on GT, NF, IIP3 and IDC by playing with W, qs.
In saturation region (only qs is needed)
Circuit equations depend on ACM2 gm’s:
Where we introduce W in the design space
Design parameters
ACM2 parameters for a fixed L
Notes: I_{SL}=\frac{I_{S0}}{W}=\mu C'_{ox}n\frac{(U_T)^2}{2L}
G_m(q_S;W)\vert_{n,\zeta,\theta}
R_F(R_0)\vert_{f_c}

## Slide 108
Inversion Level Based Method for R-Feedback LNA with ACM-2
Reducing the variables :
Starting from :
parameters
variables
VDD
VDSsat
Notes: R_F(R_0)\vert_{f_c}=R_F(q_s;W)\vert_{f_c;C_L}
I_D=I_{SL}*W*i_f
V_{DSAT}=\phi_t(\sqrt{1+i_f}+3)
G_m(q_S;W)\vert_{n,\zeta,\theta}
R_0(R_F)\vert_{f_c}
R_F(R_0)\vert_{f_c} => R_F(g_{ds},R_L)\vert_{f_c} => R_F(W,q_S,R_L)\vert_{f_c}
R_L(I_D)=\frac{V_{DD}-V_{DSAT}}{I_D}

## Slide 109
Inversion Level Based Method for R-Feedback LNA with ACM-2
Finally : ID(qs;W); RF(qs;W); R0(qs;W); GT(qs;W)
ID(qs;W)
R0(qs;W)
RF(qs;W)
Notes: R_F(R_0)\vert_{f_c}=R_F(q_s;W)\vert_{f_c;C_L}
I_D=I_{SL}*W*i_f
V_{DSAT}=\phi_t(\sqrt{1+i_f}+3)
G_m(q_S;W)\vert_{n,\zeta,\theta}
R_0(R_F)\vert_{f_c}
R_F(R_0)\vert_{f_c} => R_F(g_{ds},R_L)\vert_{f_c} => R_F(W,q_S,R_L)\vert_{f_c}
R_L(I_D)=\frac{V_{DD}-V_{DSAT}}{I_D}

## Slide 110
Inversion Level Based Method for R-Feedback LNA with ACM-2
Computing GT, F and IIP3:
Finally :
Remember :
with
Notes: I_D=I_{SL}*W*i_f
V_{DSAT}=\phi_t(\sqrt{1+i_f}+3)
G_m(q_S;W)\vert_{n,\zeta,\theta}
R_0(R_F)\vert_{f_c}
R_F(R_0)\vert_{f_c} => R_F(g_{ds},R_L)\vert_{f_c} => R_F(W,q_S,R_L)\vert_{f_c}
R_L(I_D)=\frac{V_{DD}-V_{DSAT}}{I_D}

## Slide 111
Inversion Level Based Method for R-Feedback LNA with ACM-2
Exploring the design space:
Setting GT (or NF, or IIP3) helps to build 2D plots.
=> We get the relationship qS<=>W
qS
W(mm)
=> We plot NF(W)
For a particular GT
=> We plot IIP3(W)
And We already have ID
Notes: I_{SL}=\frac{I_{S0}}{W}=\mu C'_{ox}n\frac{(U_T)^2}{2L}
G_m(q_S;W)\vert_{n,\zeta,\theta}
R_F(R_0)\vert_{f_c}

## Slide 112
Inversion Level Based Method for R-Feedback LNA with ACM-2
Setting the final value:
  We choose W, that gives qS for a given GT.
  (W;qS) gives R0, RL, ID, gmsat, VDSsat and VG
Input Matching
  With R0 , RF , gm => RP
= 50 W
  With RS and RP calculate QP
  With QP calculate CT and CGS’
  With CT calculate LG
Notes: I_{SL}=\frac{I_{S0}}{W}=\mu C'_{ox}n\frac{(U_T)^2}{2L}
G_m(q_S;W)\vert_{n,\zeta,\theta}
R_F(R_0)\vert_{f_c}

## Slide 113
Validation
Now, let’s simulate with a real PDK
Notes: I_{SL}=\frac{I_{S0}}{W}=\mu C'_{ox}n\frac{(U_T)^2}{2L}
G_m(q_S;W)\vert_{n,\zeta,\theta}
R_F(R_0)\vert_{f_c}

## Slide 114
Design and Simulation of analog/RF ICs with Open-Source CAD Tools and PDKs:
Analog Circuit Design
Pr. Márcio Cherem Schneider Department of electrical engineering Universidade Federal de Santa Catarina, Brasil

## Slide 115: Outline
Current mirrors
High-swing cascode current mirror
Current gain schemes
Current reference
Common-source amplifier

## Slide 116: Saturation voltage
VDSsat = VDS such that
=
is the saturation level
A good approximation for the saturation voltage:
UCCM
Saturation voltage versus inversion level

## Slide 117
VDD
iin
+
v
-
iout
vD
+
-
M1
M2
1:1
M1: iv converter
M2: vi converter
Basic principle VG1=VG2; VS1=VS2; VB1=VB2; vout>VDsat  ioutiin
M1=M2
Current mirrors
iD
vD
locus vD=vG
(input MOSFET)
iin
VG1
VG1=VG2
vDsat
?
?
output MOSFET
An approximation for the saturation voltage:

## Slide 118
ACM2 applied to weak inversion
WI : qS(D) << 1
ACM2 parameters: , , n, ,
UCCM

## Slide 119
VDD
Iin
+
v
-
Iout
vout
+
-
M1
M2
1:1
Error due to difference in drain voltages
ID
VD
-VA
Linear approximation
is non-physical
A simple case: error for weak inversion using ACM2
=
 for
Current mirrors

## Slide 120
Weak inversion if <1
=
Dependence of the output current (conductance) on the output voltage
VDD
iin
+
v
-
ID
vD
+
-
M1
M2
1:1
Current mirrors
(A)
2 3 4 5

## Slide 121
VDD
iin
iout
vout=vin
+
-
M1
M2
1:1
+
vin
-
Using Pelgrom’s model
In general, this is the prevailing term
Error due to mismatch
Main contributors to mismatch: &
For uncorrelated mismatch parameters:
Current mirrors
(B)
(C)
(D)
Better matching in strong inversion (for the same WL)

## Slide 122
Statistics determined
for 18 pairs of transistors.
Error due to mismatch
IB
M2
iD1
M3
iD2
M1
vD1
vD2
vD1=vD2
+
+
Current mirrors
C. Galup-Montoro et al. JSSC 2005

## Slide 123
Output conductance
Voltage gain
Current mirrors
Common gate amplifier

## Slide 124
Low-voltage cascode current mirror: lower VDD / higher output swing
VDD
M1
M2
Iin
M4
M3
VO
VDD
IB5
M5
+
VDS2
_
Io
Bias circuit
VG5
Goal: Design VG5 to bias M2 (M1) at the edge of saturation
Assume M1M2M3 M4
Cascode current mirrors
Input constraint:
VDD > VCS,min+VGS1 = VCS,min+VDS1,sat+ +VDS3
Output constraint:
Vout > VDS2,sat++ VDS4,sat for saturation of M4

## Slide 125
M1 on the edge of saturation
Cascode current mirrors
VDD
M1
M2
Iin
M4
M3
VO
VDD
IB5
M5
+
VDS2
_
Io
Bias circuit
VG5
~Vx
Vx
Find (W/L)1= (W/L)2 =(W/L)3 = (W/L)4
=
For simplicity, choose identical M1 – M4
Choose
Inversion level-based design
+
Choose

## Slide 126
2 m CMOS technology - VT0N0.55 V
Low-voltage cascode current mirror
Cascode current mirrors
V. C. Vincence, C. Galup-Montoro and M. C. Schneider, IEEE Trans. Circuits Syst. II, 2000.
P. Aguirre and F. Silveira, Proc. of SBCCI 2006.

## Slide 127
In the triode region for a long channel transistor
DC equivalence between series-connected and single transistors. The gate and
bulk terminals are common to both transistors.
Series association of transistors

## Slide 128
Example: Gain-of-16 current mirror
Current gain schemes
VDD
IIN
IOUT
1/16:1
16
(A)
VDD
IIN
IOUT
1:16
16
(B)
VDD
IIN
1/4:4
4
IOUT
4
(C)

## Slide 129
Current gain schemes
Binary division of currents
I
2R
2R
2R
2R
R
R
R
R
R
I/2
I/4
I/8
I/16
bi=0 or VDD
VDD
I
I
I/2
I/4
I/8
I/8
All transistors: same W and L

## Slide 130
In weak inversion,
Series association of conductances
Sat.
Triode
Current reference
The self-cascode MOSFET (SCM)
Notes: EMICRO II - Bahia
130

## Slide 131
Current reference
A self-biased current source (SBCS)

## Slide 132
Current reference
Thus, if4 (the inversion level of M4 ) is constant (it depends only on the geometrical ratios α12 and α34)
The reference current IB2 = IS2if2 is proportional to the specific current of M2. IS2 = ISH(W/L)2= ISHS2
Stability at the operating point:
Negative feedback > positive feedback
If M1 and M2 operate in WI :
Voff
IB2
IB2
VX
Positive feedback
Negative feedback
VX
A self-biased current source (SBCS)
Notes: .

## Slide 133
Current reference
A self-biased current source (SBCS)
The voltage following current mirror – VFCM
1:1
1:1
SCM
SCM
VF
CM

## Slide 134
VO
ID
(a)
VDD
VI
M1
+
VO
IB
CL
ID
IL
IB
VDD
(b)
Q
VGQ
VOQ
The gain is a function of technology, transistor channel length, bias current, and output voltage
Common-source amplifier
Intrinsic gain
S
D
id

## Slide 135
VDD
VI
M1
+
VO
IB
CLVD=0
ID
IL
Velocity saturation not accounted for :
VD
Triode
Common-source amplifier
Intrinsic gain
VD
ID
VD

## Slide 136
VDD
VI
M1
+
VO
IB
CL
ID
IL
Weak inversion
Common-source amplifier
Intrinsic gain
>1
>>

## Slide 137
VDD
vin
+
-
M1
M2
ID2
ID1
IL
Voltage gain (saturation):
for
CMOS inverter
For “deep” saturation:
VDD
VDD
Vout
Vin
VM
Av
Vout=Vin
ID
IM
Vin
Common-source amplifier

## Slide 138: Acknowledgments
This project has received funding from the European Union’s Horizon Europe research and innovation programme under the HORIZON-KDT-JU-2023-1-IA grant agreement No 101139785